Kubernetes Cluster Setup with kubeadm and Calico CNI
Complete Guide for AWS Linux Instances
Prerequisites
AWS Infrastructure Requirements
- 3 EC2 Instances (Amazon Linux 2023)
  - 1 Control Plane (Master)
  - 2 Worker Nodes
- Instance Type: t2.medium or larger (minimum 2 CPUs, 2GB RAM)
- Storage: At least 20GB root volume
Security Group Configuration
Configure the security group to allow the following traffic:
For All Nodes:
- All traffic between nodes (recommended for testing)
- Source: Same Security Group ID or VPC CIDR (172.31.0.0/16)
Specific Ports (if not using "All Traffic"):
Master Node - Inbound:
- TCP 6443 - Kubernetes API server
- TCP 2379-2380 - etcd server client API
- TCP 10250 - Kubelet API
- TCP 10251 - kube-scheduler
- TCP 10252 - kube-controller-manager
Worker Nodes - Inbound:
- TCP 10250 - Kubelet API
- TCP 30000-32767 - NodePort Services
Calico Requirements:
- TCP 179 - BGP
- UDP 4789 - VXLAN (if using VXLAN mode)

Step 1: Prepare All Nodes (Master + Workers)
Run these commands on ALL THREE NODES (master + worker1 + worker2):
1.1 Update System
bash
sudo yum update -y
1.2 Disable Swap
Kubernetes requires swap to be disabled:
bash
# Disable swap immediately
sudo swapoff -a

# Disable swap permanently
sudo sed -i '/ swap / s/^/#/' /etc/fstab

# Verify swap is off
free -h
# Swap line should show 0B
1.3 Load Required Kernel Modules
bash
# Create configuration file for modules
cat <<EOF | sudo tee /etc/modules-load.d/k8s.conf
overlay
br_netfilter
EOF

# Load modules immediately
sudo modprobe overlay
sudo modprobe br_netfilter

# Verify modules are loaded
lsmod | grep overlay
lsmod | grep br_netfilter
Why these modules?
- overlay: Required for container storage (containerd uses overlay2)
- br_netfilter: Required for iptables to see bridged network traffic
1.4 Configure sysctl Parameters
bash
# Create sysctl configuration
cat <<EOF | sudo tee /etc/sysctl.d/k8s.conf
net.bridge.bridge-nf-call-iptables = 1
net.bridge.bridge-nf-call-ip6tables = 1
net.ipv4.ip_forward = 1
EOF

# Apply sysctl parameters
sudo sysctl --system
What these do:
- net.bridge.bridge-nf-call-iptables: Allow iptables to process bridged IPv4 traffic
- net.bridge.bridge-nf-call-ip6tables: Allow iptables to process bridged IPv6 traffic
- net.ipv4.ip_forward: Enable IP forwarding (required for pod networking)
1.5 Install containerd
bash
# Remove any broken Docker repos (if they exist)
sudo rm -f /etc/yum.repos.d/docker-ce-stable.repo

# Install containerd from Amazon Linux repository
sudo yum install -y containerd

# Create containerd configuration directory
sudo mkdir -p /etc/containerd

# Generate default configuration
sudo containerd config default | sudo tee /etc/containerd/config.toml

# Enable SystemdCgroup (CRITICAL for Kubernetes)
sudo sed -i 's/SystemdCgroup = false/SystemdCgroup = true/' /etc/containerd/config.toml

# Start and enable containerd
sudo systemctl restart containerd
sudo systemctl enable containerd

# Verify containerd is running
sudo systemctl status containerd
Why SystemdCgroup? Kubernetes uses systemd for cgroup management. This must be enabled in containerd.
1.6 Add Kubernetes Repository
bash
# Add Kubernetes yum repository
cat <<EOF | sudo tee /etc/yum.repos.d/kubernetes.repo
[kubernetes]
name=Kubernetes
baseurl=https://pkgs.k8s.io/core:/stable:/v1.28/rpm/
enabled=1
gpgcheck=1
gpgkey=https://pkgs.k8s.io/core:/stable:/v1.28/rpm/repodata/repomd.xml.key
exclude=kubelet kubeadm kubectl cri-tools kubernetes-cni
EOF
1.7 Install Kubernetes Components
bash
# Install kubeadm, kubelet, and kubectl
sudo yum install -y kubelet kubeadm kubectl --disableexcludes=kubernetes

# Enable kubelet (will start after cluster initialization)
sudo systemctl enable --now kubelet
Components installed:
- kubeadm: Tool to bootstrap the cluster
- kubelet: Node agent that runs on every node
- kubectl: Command-line tool to interact with the cluster
1.8 Verify Installation
bash
# Check containerd is running
sudo systemctl is-active containerd

# Check kubelet is enabled
sudo systemctl is-enabled kubelet

# Verify modules are loaded
lsmod | grep br_netfilter
lsmod | grep overlay
All checks should return positive results.

Step 2: Initialize Control Plane (Master Only)
Run these commands ONLY on the MASTER NODE:
2.1 Get Master Node IP Address
bash
# Find your master node's private IP
hostname -I | awk '{print $1}'
# Example output: 172.31.9.150
2.2 Initialize the Cluster
bash
# Replace <MASTER_IP> with your actual IP from step 2.1
sudo kubeadm init --pod-network-cidr=192.168.0.0/16 --apiserver-advertise-address=<MASTER_IP>

# Example:
# sudo kubeadm init --pod-network-cidr=192.168.0.0/16 --apiserver-advertise-address=172.31.9.150
Parameters explained:
- --pod-network-cidr=192.168.0.0/16: IP range for pod network (required by Calico)
- --apiserver-advertise-address: IP address the API server will advertise
IMPORTANT: Save the join command that appears at the end! It looks like:
kubeadm join 172.31.9.150:6443 --token <token> \
  --discovery-token-ca-cert-hash sha256:<hash>
2.3 Configure kubectl for Regular User
bash
# Create kube config directory
mkdir -p $HOME/.kube

# Copy admin configuration
sudo cp -i /etc/kubernetes/admin.conf $HOME/.kube/config

# Change ownership to current user
sudo chown $(id -u):$(id -g) $HOME/.kube/config
2.4 Verify Control Plane
bash
# Check nodes (will show NotReady - this is normal before CNI installation)
kubectl get nodes

# Check system pods
kubectl get pods -n kube-system

Step 3: Install Calico CNI (Master Only)
CNI (Container Network Interface) is required for pod networking.
3.1 Install Calico
bash
# Download and apply Calico manifest
kubectl apply -f https://raw.githubusercontent.com/projectcalico/calico/v3.26.1/manifests/calico.yaml
3.2 Wait for Calico Pods
bash
# Watch Calico pods starting (press Ctrl+C to exit)
kubectl get pods -n kube-system -w

# Or check status
kubectl get pods -n kube-system | grep calico
Wait until all Calico pods show Running status (typically 2-3 minutes).
3.3 Verify Master Node is Ready
bash
# Check node status (should now show Ready)
kubectl get nodes

# Expected output:
# NAME STATUS ROLES AGE VERSION
# k8s-master Ready control-plane 5m v1.28.15

Step 4: Join Worker Nodes (Workers Only)
Run these commands on EACH WORKER NODE (worker1 and worker2):
4.1 Join the Cluster
bash
# Use the join command from Step 2.2
sudo kubeadm join <MASTER_IP>:6443 --token <token> \
  --discovery-token-ca-cert-hash sha256:<hash>

# Example:
# sudo kubeadm join 172.31.9.150:6443 --token ou2eat.w9gwb7crbdt4j9kn \
# --discovery-token-ca-cert-hash sha256:03a3e4f78c49e1c61003a3ebc7495d600e266f3de8b7b553c7d63716da1c3477
If token expired (tokens last 24 hours):
bash
# Generate new token on master node
kubeadm token create --print-join-command
4.2 Verify Join Success
You should see output like:
This node has joined the cluster:
* Certificate signing request was sent to apiserver and a response was received.
* The Kubelet was informed of the new secure connection details.

Step 5: Verify Cluster
Run these commands on the MASTER NODE:
5.1 Check All Nodes
bash
# List all nodes
kubectl get nodes

# Expected output (all nodes should show Ready):
# NAME STATUS ROLES AGE VERSION
# k8s-master Ready control-plane 10m v1.28.15
# k8s-worker1 Ready <none> 2m v1.28.15
# k8s-worker2 Ready <none> 1m v1.28.15
5.2 Check All Pods
bash
# Check all system pods
kubectl get pods --all-namespaces

# Check specifically Calico pods on all nodes
kubectl get pods -n kube-system -o wide | grep calico
5.3 Get Cluster Information
bash
# Display cluster info
kubectl cluster-info

# Display detailed node information
kubectl get nodes -o wide

5.4 Test Deployment (Optional)
bash
# Create a test deployment
kubectl create deployment nginx --image=nginx

# Check deployment
kubectl get deployments

# Check pods
kubectl get pods

# Expose deployment
kubectl expose deployment nginx --port=80 --type=NodePort

# Get service details
kubectl get svc nginx

Troubleshooting
Common Issues and Solutions
Issue 1: Port 6443 Already in Use
Error: [ERROR Port-6443]: Port 6443 is in use
Solution:
bash
# Reset kubeadm
sudo kubeadm reset -f

# Clean up files
sudo rm -rf /etc/cni/net.d
sudo rm -rf $HOME/.kube

# Restart services
sudo systemctl restart containerd
sudo systemctl restart kubelet

# Try init again
Issue 2: Worker Node Join Hangs
Cause: Security group blocking traffic
Solution:
1. Check AWS Security Group allows:
  1. All traffic between nodes OR
  2. At minimum: ports 6443, 10250 from workers to master
2. Test connectivity:
bash
# On worker node
telnet <MASTER_IP> 6443
# Should connect successfully
Issue 3: Node Already Exists
Error: a Node with name "k8s-worker1" and status "Ready" already exists
Solution:
bash
# On master - delete the node
kubectl delete node k8s-worker1

# On worker - reset completely
sudo kubeadm reset -f
sudo rm -rf /etc/kubernetes
sudo rm -rf /var/lib/kubelet
sudo systemctl restart containerd
sudo systemctl restart kubelet

# Try join again
Issue 4: Nodes Stuck in NotReady State
Cause: CNI not installed or not working
Solution:
bash
# Check Calico pods
kubectl get pods -n kube-system | grep calico

# If pods are not running, reinstall Calico
kubectl delete -f https://raw.githubusercontent.com/projectcalico/calico/v3.26.1/manifests/calico.yaml
kubectl apply -f https://raw.githubusercontent.com/projectcalico/calico/v3.26.1/manifests/calico.yaml
Issue 5: containerd Not Installing
Error: No match for argument: containerd.io
Solution:
bash
# Remove Docker repo
sudo rm -f /etc/yum.repos.d/docker-ce-stable.repo

# Install from Amazon Linux repo
sudo yum install -y containerd
Issue 6: Token Expired
Symptoms: Join fails with authentication errors
Solution:
bash
# On master - generate new token
kubeadm token create --print-join-command

# Use the new command on worker nodes

Important Commands
Cluster Management
bash
# View cluster info
kubectl cluster-info

# View nodes
kubectl get nodes
kubectl get nodes -o wide

# View all pods across all namespaces
kubectl get pods --all-namespaces
kubectl get pods -A

# Describe a node
kubectl describe node <node-name>
Token Management
bash
# List tokens
kubeadm token list

# Create new token
kubeadm token create

# Create token with join command
kubeadm token create --print-join-command
Node Management
bash
# Remove a node from cluster (run on master)
kubectl drain <node-name> --ignore-daemonsets --delete-emptydir-data
kubectl delete node <node-name>

# Reset a node (run on the node itself)
sudo kubeadm reset -f

Pod and Service Management
bash
# Create deployment
kubectl create deployment <name> --image=<image>

# Scale deployment
kubectl scale deployment <name> --replicas=3

# Expose deployment
kubectl expose deployment <name> --port=80 --type=NodePort

# Get services
kubectl get svc

# Delete deployment
kubectl delete deployment <name>

Logs and Debugging
bash
# View kubelet logs
sudo journalctl -u kubelet -f

# View containerd logs
sudo journalctl -u containerd -f

# View pod logs
kubectl logs <pod-name>

# Exec into pod
kubectl exec -it <pod-name> -- /bin/bash

# Describe pod (useful for troubleshooting)
kubectl describe pod <pod-name>

System Status
bash
# Check component status
kubectl get componentstatuses

# Check system pods
kubectl get pods -n kube-system

# View events
kubectl get events --all-namespaces --sort-by='.lastTimestamp'

Architecture Components
Control Plane Components (Master Node)
- kube-apiserver: Exposes the Kubernetes API (port 6443)
- etcd: Key-value store for cluster data (ports 2379-2380)
- kube-scheduler: Assigns pods to nodes (port 10251)
- kube-controller-manager: Runs controller processes (port 10252)
- cloud-controller-manager: Interacts with cloud provider APIs
Node Components (All Nodes)
- kubelet: Agent that runs on each node (port 10250)
- kube-proxy: Network proxy maintaining network rules
- Container Runtime: containerd (running containers)
Add-ons
- Calico: CNI plugin for pod networking
- CoreDNS: DNS server for service discovery

Network Flow
Pod-to-Pod Communication
Pod A (192.168.1.5) → Calico CNI → Node Network → Calico CNI → Pod B (192.168.2.10)
External Access to Service
External Client → NodePort (30000-32767) → kube-proxy → Service → Pod
Pod-to-API Server
Pod → Service (kubernetes.default) → API Server (6443)

Best Practices
1. Security Groups: Use VPC CIDR or Security Group IDs instead of 0.0.0.0/0
2. Regular Updates: Keep Kubernetes components updated
3. Backup etcd: Regular backups of etcd data
4. Resource Limits: Set resource requests and limits for pods
5. Monitoring: Implement monitoring (Prometheus, Grafana)
6. High Availability: For production, use multiple master nodes
7. Node Sizing: Use appropriate instance sizes (t2.medium minimum)
8. Storage: Use persistent volumes for stateful applications

Next Steps
1. Deploy Applications: Start deploying your containerized applications
2. Set Up Ingress: Install Nginx Ingress Controller for HTTP routing
3. Add Monitoring: Install Prometheus and Grafana
4. Configure Storage: Set up persistent volume provisioners
5. Implement CI/CD: Integrate with Jenkins, GitLab, or ArgoCD
6. Security Hardening: Implement RBAC, Network Policies, Pod Security Standards